## Slide 1: Fluid dynamics and beyond: opportunities with the lattice Boltzmann method
Alessandro De Rosis
Lecturer in Virtual Engineering
Department of Fluids and Environment
The University of Manchester
alessandro.derosis@manchester.ac.uk
De Rosis & Enan
Phys Fluids 2021
De Rosis
Europhys Lett 2018
Notes: bhauhfuasd

## Slide 2
The 10-orders-of-magnitude hierarchy
Microscopic
Kinetic
Macroscopic
Time scale [s]
Length scale [m]
100
10-3
10-6
10-9
10-2
10-3
10-4
10-5
10-6
10-7
10-8
10-9
Finite difference method
Finite volume method
Element free Galerkin
Dissipative particle dynamics
Lattice Boltzmann method (LBM)
Off-lattice Monte Carlo
Molecular dynamics
4
v
v
Numerical simulations of fluid dynamics

## Slide 3: Lattice Boltzmann method
Lattice
Boltzmann
(Kinetic theory)
5

## Slide 4
Macroscopic and microscopic scales
6
At the macroscopic level, a fluid is a continuous material with some properties and it obeys the Navier-Stokes equations. Pressure, density and velocity are continuous variables which can be measured.
Linking macro and micro worlds

## Slide 5
Macroscopic and microscopic scales
7
At the microscopic level, we play another game. Here, the fluid is an ensemble of molecules with an unpredictable (chaotic) behaviour and it loses its apparent global coherence. The apparent continuity of the fluid is broken.
Establishing the link between macro and micro worlds is instrumental to a better understanding of the fluid behaviour.
Linking macro and micro worlds

## Slide 6
Macroscopic and microscopic scales
8
At the macroscopic level, we can visualise and measure density and velocity.
At the microscopic level, how can we define density and velocity while molecules move in a disordered way?
Linking macro and micro worlds

## Slide 7
Density and velocity at the microscopic scale
9
Particles move in an apparent disordered and random manner.
However, this apparent chaos hides info about the macroscopic properties.
Density is easy to get:
: number of particles
: mass of a particle
: control volume
For the velocity, we assume isotropy: the velocity vector of a particle can point in any direction with the same probability.
The average velocity magnitude is
Temperature should be considered.
Boltzmann tells us that the internal microscopic kinetic energy is
where is a constant.

## Slide 8
Boltzmann-Maxwell distribution of speed
10
If we consider that each particle individually possesses a velocity according to an indivually indeterminate probability law, the central limit theorem tells us that the process obeys the Gaussian normal law.
For a perfect gas, the problem is governed by Maxwell equilibrium distribution:

## Slide 9
Boltzmann equation
11
The probability to find a particle moving with velocity at the position at time is given by the distribution function
At low Mach number and in absence of collision, the differential of is conserved:
The Taylor development leads to
In presence of collision, this must account for the variations of probability distribution:
The collision operator can be written as the relaxation to a local equilibrium (Bhatnagar-Gross-Krook [BGK] approximation):

## Slide 10
Discrete Boltzmann equation
12
We need to solve numerically
By discretising space, time and particle velocity:
where
Macroscopic variables are obtained as
D2Q9

## Slide 11
Discrete Boltzmann equation
12
We need to solve numerically
By discretising space, time and particle velocity:
where
Macroscopic variables are obtained as
D3Q27
D2Q9

## Slide 12
Why LBM?
13
Notes: In addition to some popular open-source codes, during the last decade several companies have been putting a very significant amount of resources in the LBM technology. Among its advantages, it is worth to mention the intelligibility of its algorithmic procedure, the simplicity of imposing boundary conditions and the very high computational efficiency. However, the thing I like the most is its natural suitability for multiphysics.

## Slide 13
A simple (yet naive) LBM code
14

## Slide 14
A simple (yet naive) LBM code
14
Grid loop

## Slide 15
A simple (yet naive) LBM code
14
Compute macroscopic variables
Grid loop

## Slide 16
A simple (yet naive) LBM code
14
Evaluate equilibrium populations
Compute macroscopic variables
Grid loop

## Slide 17
A simple (yet naive) LBM code
14
Grid loop
Compute macroscopic variables
Evaluate equilibrium populations
Collision & Streaming